## Slide 1
Rise of the Nodebots
Presented By
JOEL LORD
ConUHacks
January 21st, 2017

## Slide 2: About me
Joel Lord
Javascript Junkie
Technology enthusiast
Tinkerer

## Slide 3: What about your friend there?
My nodebot

## Slide 4
Agenda
Demo
Hardware
Software
Setting up the Arduino board
Setting up the project
Building a Hello World!
Building the Night light

## Slide 5: Demo Time!
CROSS YOUR FINGERS
Notes: Demo of something that can be done with J5
Demo of the final product

## Slide 6: Demo
A Simple and cumbersome night light

## Slide 7: Your Kit
CHECK YOUR PARTS

## Slide 8: Your Kit
LIST OF COMPONENTS
1 Arduino board
1 USB Cable
1 Breadboard
4 Jumper Cables
2 Red LEDs
2 220 ohms Resistors
1 Photoresistor
1 1k ohms Resistor

## Slide 9: Hardware
COVERING THE BASICS

## Slide 10: Hardware
Arduino
Open Source hardware and software
Uses an ATMega programmable chip
Programmable in C
We can use the serial port to send instructions using the Standard Firmata (https://github.com/firmata/arduino)

## Slide 11: Hardware
HOW BREADBOARD WORKS

## Slide 12: Hardware
RESISTORS AND OHMS LAW

## Slide 13: Software
COVERING THE BASICS

## Slide 14: Software
Node.js
JavaScript runtime built on Chrome's V8 JavaScript engine.
Open Source and available freely
Available at https://nodejs.org/

## Slide 15: Software
NPM
Node Package Manager
Comes out of the box with NodeJs
Available at https://www.npmjs.com/

## Slide 16: Software
JoHNNY-FIVE
Available through npm
Documentation at http://johnny-five.io/

## Slide 17: Setting up the Arduino
GETTING SERIOUS

## Slide 18: Setting Up the Arduino
Install the Standard Firmata
To enable communication with the serial port, you need the Standard Firmata Plus installated
https://github.com/firmata/arduino
All the boards today come pre-configured
Still, here is how to install it

## Slide 19: Setting up the project
GETTING SERIOUS

## Slide 20: Setting Up the project
NPM INIT AND DEPENDENCY INSTALL
Create a new project using npm init
Install Johnny-Five using npm install --save johnny-five

## Slide 21: Setting up the project
NPM INIT
> npm init
name: (test)
version: (1.0.0)
description:
entry point: (index.js)
test command:
git repository:
keywords:
author:
license: (ISC)
About to write to /Users/jlord/Documents/Projects/test/package.json:
{
"name": "test",
"version": "1.0.0",
"description": "",
"main": "index.js",
"scripts": {
"test": "echo \"Error: no test specified\" && exit 1"
},
"author": "",
"license": "ISC"
}
Is this ok? (yes)

## Slide 22: Setting up the project
NPM install
> npm install --save johnny-five
npm WARN package.json test@1.0.0 No description
npm WARN package.json test@1.0.0 No repository field.
npm WARN package.json test@1.0.0 No README data
\
> serialport@4.0.7 install /Users/jlord/Documents/Projects/test/node_modules/johnny-five/node_modules/serialport
> node-pre-gyp install --fallback-to-build
[serialport] Success: "/Users/jlord/Documents/Projects/test/node_modules/johnny-five/node_modules/serialport/build/Release/serialport.node" is installed via remote
johnny-five@0.10.6 node_modules/johnny-five
├── lodash.debounce@4.0.8
├── lodash.clonedeep@4.5.0
├── ease-component@1.0.0
├── color-convert@1.2.2
├── browser-serialport@2.1.0
├── temporal@0.5.0
├── nanotimer@0.3.10
├── firmata@0.15.0
├── chalk@1.1.3 (escape-string-regexp@1.0.5, ansi-styles@2.2.1, supports-color@2.0.0, has-ansi@2.0.0, strip-ansi@3.0.1)
├── es6-shim@0.35.2
└── serialport@4.0.7 (bindings@1.2.1, commander@2.9.0, lie@3.1.0, debug@2.6.0, nan@2.5.0, object.assign@4.0.4)

## Slide 23: Hello World !
GETTING SERIOUS

## Slide 24: Hello World
Wiring up the lED
Wire up the LED

## Slide 25: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 26: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 27: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 28: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 29: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 30: Hello World
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
led.blink(500);
});

## Slide 31: Hello World
Running the script
Run the Node script
node hello.js
1484955651472 Device(s) /dev/cu.usbmodem1421
1484955651484 Connected /dev/cu.usbmodem1421
1484955653114 Repl Initialized
>>

## Slide 32: Finishing the Night light
GETTING SERIOUS

## Slide 33: Night Light
The Code
Wire up the Photoresistor and tweak the layout

## Slide 34: Night Light
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 35: Night Light
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 36: Night Light
The Code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 37: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 38: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 39: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 40: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 41: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 42: Night Light
The code
Create the index.js file
var j5 = require("johnny-five");
var board = new j5.Board();
board.on("ready", function() {
var led = new j5.Led(13);
var sensor = new j5.Sensor("A0");
sensor.on("change", function() {
if (sensor.value > 750) {
led.on();
} else {
led.off();
}
});
});

## Slide 43: Night Light
Running the script
Run the Node script
node index.js
1484955651472 Device(s) /dev/cu.usbmodem1421
1484955651484 Connected /dev/cu.usbmodem1421
1484955653114 Repl Initialized
>>

## Slide 44
The End !
Questions ?
Joel Lord
January 21st, 2017
Twitter: @joel__lord
Github: http://github.com/joellord